Cisco 79xx Series IP Phones Upgrade Path

POS30200

POS30203

POS3-03-0-00

POS3-04-4-00

POS3-05-3-00

POS3-06-0-00

POS3-07-0-00

POS3-07-4-00

On B2 Server (under drive D:/Asterisk Files/Upgrade Files):

- Edit OS79xx.txt to match image version

- Edit SIPDEFAULT.CNF to match image version (1st line only).

- Creat new SIP000[MAC].CNF by copying an existing file.

Change display name to the proper user near the bottom.

Change the TFTP server directory to D:/Asterisk Files/Upgrade

Reboot the Cisco phone (unplug & replug power or network cable).

Repeat each step above for all 4 images.

Change TFTP directory back to D:/Asterisk Files when done with upgrades.

Note:	Check firmware version on Cisco phone to confirm if upgrade took effect.

Cisco 79xx Series IP Phones Setup

- Press * * # and Settings (checkbox) button to unlock Cisco phone.

Display will show an unlock icon on upper right-hand side.

If Cisco phone needs unlocking, then enter “123” as password.

2)  Edit network configuration on Cisco phone as follows:

- DHCP Enabled = NO

- IP Address = IP Address assigned

- Subnet Mask = 255.255.255.0

- TFTP = 192.168.0.254 (or TFTP server address if different)

- Default Router = 192.168.1.253 (or Default Router address if different)

- Confirm that both primary and secondary DNS servers were assigned

- DNS1 = 192.168.0.30

- DNS2 = 24.75.46.242

4)  Reboot Cisco phone (unplug & replug power or network cable).